Chlorohydrocarbon process

Industry: 	Bulk chemicals

Process:	Production of chlorohydrocarbons

Technology:	Reactor, distillation, heating, cooling

Application:	Raw material for CFH and silicone

Short process description:

Methyl chloride reacts with gaseous chlorine into methylene chloride, chloroform en tetrachloride. The products are cooled in three steps down to -15 (C. HCl is still gaseous and is separated. The other products are separated in distillation columns (see figure 1).

CH3Cl + Cl2 	( HCl + CH2Cl2 (methylenechloride)

CH2Cl2 + Cl2	( HCl + CHCl3 (chloroform)

CHCl3 + Cl2 	( HCl + CCl4 (tetrachloride)

Figure 1: Production process for chlorohydrocarbons

Exergy analysis:

| Part of process | Exergy loss (MW) | Cause |
| --- | --- | --- |
| Reactor | 1.9 | Chemical |
| Quench | 1.0 | Mixing of hot and cold streams |
| First cooler | 1.0 | High discharge temperature of cooling water |
| Distillation columns | 5.0 | Temperature difference in condenser en reboiler |
| Remaining | 0.9 | - |
| Total | 9.8 |

Table 1: Exergy loss during the production of chlorohydrocarbons

Process modifications

Recover heat of reaction (450 (C) to produce high-pressure steam in stead of cooling with cooling water. (see figure 2)

Raise cooling temperature freon from  -40 (C to -38 (C

Reduce cooling power by recycling cold streams

Evaporate chlorine at 1 bar(a) instead of 10 bar(a) ( use air in stead of steam

Combining 2 distillation columns ( less condensing and evaporating

Energy savings:

Process modification

Savings steam

[ton/h]

Savings electricity

| [kW] |
| --- |
| 1. Heat of reaction | 4 | - |
| 2. Cooling temperature | - | - |
| 3. Recycling cold streams | - | 51 |
| 4. Evaporating with air | 1 | 54 |
| 5. Combining distillation columns | 4 | - |

Table 2: Energy savings of the proposed process modifications

Possibilities for applications in other industries

Chemicals

Figure 2: Process modification 1: Recovering heat of reaction

Food industry

Keywords:

Bulk chemicals, distillation, cooling, chlorohydrocarbons, chloroform, tetrachloride